How to Jump Start a Vehicle:

When your battery is dead, using the battery from another car is a great way to save you from calling out a tow truck, but it is vital that you connect the terminals correctly and follow these instructions in the right order.

- Do not jump-start your engine if the battery is frozen, the battery casing is cracked, or the battery has been unused for several days.

- Park the source vehicle (the car that is working correctly) close to the dead one, but do NOT let them touch. Turn off both ignitions.

- Connect the positive terminal (marked POS or +) on the dead battery to the positive terminal on the source battery with the RED jump lead.

- Connect the BLACK jump lead to the negative terminal (marked NEG or -) of the source battery and attach the other end to the engine block of the dead car, as far away from the dead battery as possible.

- Do NOT allow the black and red clamps to touch each other.

- Start the engine of the source car, and then attempt to start the dead car.  If it doesn’t start immediately, wait 10 seconds and try again.  If it still fails to start after repeated attempts, STOP or you may damage the starter motor.

- If the car starts, keep the engine running. Don’t turn it off until you reach your destination.